## Slide 1: Throttle Copter
David DeTomaso
Gary Crum
Justin McDowell
Wes Edens

## Slide 2: Description
Helicopter Flying Arcade Game
Button Controls the ‘flight’ of the helicopter and causes it to fly higher, gravity (letting go of button) causes it to fall
If the user hits the floor/ceiling/obstacle, game over
Level will shrink as time goes on, making it harder
Sound during game play
Using VGA Monitor

## Slide 3: Description

## Slide 4: System Diagram
Number of Slices:
743 out of 4656 15%

## Slide 5: Resource Utilization
 | ROMs | Adder | Counters | Registers | Comparators | Multiplexers | Xors | FSM
VGA Controller |  | 2 | 3 | 21 | 8 |  |  | 
VGA Mixer |  |  |  | 8 |  |  |  | 
Debounce |  | 1 |  | 23 | 1 |  |  | 
Copter Gen | 2 | 5 |  | 62 | 4 | 2 |  | 
Scene Gen |  | 10 |  | 152 | 9 |  | 1 | 1
Collision Detect |  |  |  | 3 |  |  |  | 
Game Control |  | 1 | 1 | 38 |  |  |  | 1
Score | 2 | 5 | 1 | 9 | 8 | 5 |  | 
Sound |  | 2 | 2 | 51 | 1 |  |  | 1
Copter Position |  |  | 1 | 1 |  |  |  | 
Total | 4 | 26 | 8 | 368 | 31 | 7 | 1 | 3

## Slide 6: Division of Work
David –
  Scene Generation
Justin –
  Audio
Gary –
  Game Logic
Wes –
  Scorekeeping

## Slide 7: Score Module
Module that paints text on the screen
Needs a position to place the text
Needs a way of incrementing the numeric value
Outputs the RGB value for a given x,y pixel location in the screen

## Slide 8: Font Rom Creation
Create a text file of each of the letters to be used.
Decide on a height/width of each char
Create a mask for each character
  Blank space means 0
  Any other char mean 1
Create a postscript font file from this file (c code)
Perl script to create the .coe memory initialization file
c code obtained at: http://nafe.sourceforge.net/

## Slide 9: Score Module

## Slide 10: Scene Generation - Storage
In total this will require 64 bits per column:
  Cave Top and Bottom have extra 12 bits of decimal precision so that arbitrary slopes can be represented in the lines that connection points on the ceiling and floor.
63…42
41…20
19…10
9…0
Cave
Top
Cave
Bottom
Block Top
Block
Bottom

## Slide 11: Scene Generation - Readout
Col
Offset
Ceiling
Floor
Block Top
Block Bottom
<=
>=
>=
<=
OR
Row
Row
Row
Row
Pixel is Green

## Slide 12: Scene Generation - Writing
A state machine handles the writing to block memory to add columns.
  Triggered by an update pulse between frames
PreStart
Start
S2
S3
S4
S5
Waiting

## Slide 13: Game Control FSM
Seven States
Allows game setup after Reset and New Game
Starts and Stops other Modules
Provides 'safe' continuation for New Game

## Slide 14: Copter Generation
Two Image Constants – Up and Down
Process Detects when Pixel is in Copter 'Box'

## Slide 15: VGA Mixer
Layers Graphics:
  0 – Implied Background
  1 – Scene/Obstacle
  2 – Copter
  3 - Score

## Slide 16: Sound and LED's
Features
  Jaws theme music during game play
  Scrolling LED's during game play
  “Game Over” sound triggered by crash
  All LED's flashing at end of game

## Slide 17: Sound and LED's
Components
  Digital Clock Manager
  Digital to Analog Converter
  Sine Lookup Table
  Lowpass Filter

## Slide 18: Sound and LED's
Utilization
  One of four DCM's (25%)
  13 of 232 IOBs (5%)
  2 of 24 GCLKs (8%)
  One six state FSM

## Slide 19: Questions
?